## Slide 1
SEPT 2026
INJEQT: Improved Magic-State Injection Protocol for Fault-Tolerant Quantum Extractor Architectures
Sayam Sethi, Sahil Khan, Aditi Awasthi, Abhinav Anand, Jonathan Mark Baker

## Slide 2
Recent works[27,9,31] have proposed architectural designs and a PBC (Pauli-Based Computation) compilation pipeline
These techniques enable universal quantum computation on any high-rate code
Still need to address
  mechanism and cost of resource state generation + injection
  construction of adapters for inter-module operations
[27] https://arxiv.org/abs/2410.03628
[9] https://arxiv.org/abs/2503.10390
[31] https://arxiv.org/abs/2506.03094
Extractor-Based Architectures

## Slide 3: Compiling to Extractor Architecture
Start with a Clifford + Rz/T circuit
Commute all Cliffords to the end to obtain Pauli Product Rotations/Measurements (PPRs/PPMs)
Compile the PPRs and PPMs into extractor instructions

## Slide 4: Extractor ISA on the Gross Code (Tour de Gross)
Inter-module instructions are the most erroneous
Magic state preparation can be done by:
  Multiple |𝑇⟩ states ( injections for a synthesis fidelity )
  Single Rz state
Each injection also requires an inter-module measurement
[31] https://arxiv.org/abs/2506.03094
[7] http://arxiv.org/abs/2409.17595
[1] https://arxiv.org/abs/2303.13181v1
[23] http://arxiv.org/abs/2408.14708
requires a correction Rz with 50% probability

## Slide 5
The error incurred by each factory is:
  (in expectation)
If we want ,
 | LER of the factory
 | LER of the factory
 | LER of the gate
 | LER of the gate
 | Number of injections
Error Analysis – Deciding between and
Notes: Rz injections fail with 50% probability

## Slide 6
Error Analysis – wins over at current LER estimates
Notes: We can achieve better Rz error rates than T via INJEQT at current error estimates

## Slide 7: INJEQT: 2-Level Factory Design
Want: construct states with low error in auxiliary code
Lattice surgery error in surface code scales as [31]
Therefore, we can prepare low-error Rz states using 2-level factory design
[31] https://arxiv.org/abs/2506.03094
Note: [17] http://arxiv.org/abs/2604.20013 is a same-time work with a similar construction

## Slide 8: INJEQT: Timing Analysis
For tour de gross (TDG), each PPR takes:
The expected time for PPR execution in INJEQT is:
where ( depends on the choice of surface code technology)
We can now compute,
Despite being small, and therefore
Therefore, naïve implementation of INJEQT is sub-optimal in time
 | #steps for the factory
 | #steps for the factory
 | #steps for inter-module measurements
 | #steps for injection in surface code
 | Number of injections
 | #steps for INJEQT : TDG (ratio)
 | #steps for inter-module measurements
 | #steps for INJEQT : TDG (ratio)
Notes: Okay so we addressed error rates, what about time?

## Slide 9: INJEQT: Improve Performance by Pre-Fetching
Recall: injection fails with 50% probability
Pre-fetch correction states using R factories
What do we do with unused states?
  Usable for next rotation? Keep them
  Else, discard
No stalls if: #injections (w.p. )
As , this gives
If we prepare in parallel with other ops,
 | #steps for the factory
 | #steps for the factory
 | #steps for inter-module measurements
 | #steps for injection in surface code
 | Number of injections
 | #steps for INJEQT : TDG (ratio)
 | #steps for inter-module measurements
 | #steps for INJEQT : TDG (ratio)
Notes: Well, that’s bad, so how do we fix this?

## Slide 10: Evaluation Methodology
We use the error rates and timing models from prior work
Benchmarks are obtained from QASMBench suite
states are synthesized into states using Gridsynth
  Precision for each benchmark is chosen such that total synthesis error has the same leading order as the total error from in-module, inter-module, injections etc.
  For the benchmark circuits we consider, the synthesis precisions are between
We run 20 trials to model non-deterministic execution in INJEQT, cultivation and STAR
We compute the total program error rate using a first order approximation
Surface code operations are modelled for both lattice surgery and transversal injections
For INJEQT, we evaluate for , and report the value which optimizes the metric
Notes: Well, that’s bad, so how do we fix this?

## Slide 11
Evaluation – Distillation Factory
Up to 12.5% improvement in total error
Up to 7x improvement in space-time
Up to 13x improvement in wall-clock time
With at most an 8% increase in #physical qubits

## Slide 12
Evaluation – Cultivation Factory
Up to 5x improvement in space-time
Up to 8.8x improvement in wall-clock time
With at most a 25% increase in #physical qubits
Up to 22x improvement in total error

## Slide 13
Up to 16x improvement in space-time
Up to 12x improvement in wall-clock time
Up to 11% improvement in #physical qubits
Up to 18x improvement in total error
Evaluation – STAR Factory

## Slide 14
Evaluation – Sensitivity to #Factories (R)
Different benchmarks have different operating points
Improvements saturate with increasing factories
Monotonic increase in #qubits
No change

## Slide 15
Evaluation – Sensitivity to #Factories (R)
Optimal R for most benchmarks is ~7-10
Some benchmarks achieve maximal speedup with fewer factories

## Slide 16: Conclusion
Extractor-based architectures are bottlenecked by:
  sequential execution and high error rates of inter-module measurements
  Resource state injection contributes over 90% of the total program error
We propose INJEQT, a 2-level factory design:
  first prepare Rz states in an auxiliary code,
  then inject the Rz state onto the extractor module
INJEQT improves program error rates by up to 12.5% for distillation, up to 22x for cultivation, and up to 18x for STAR factories
To improve latency of the 2-level factory, we introduce a pre-fetching technique
  prepare the Rz state and potential corrections in parallel with other extractor operations
This approach improves the wall-clock times by up to 13x for distillation, 8.8x for cultivation and 12x for STAR

## Slide 17: Thanks!
Code available